Documentation for pCorrect as it is written for SquirrelGPU.

pCorrect is the name of an implementation of a perspective correction algorithm using basic camera data. It accepts camera data and an image (to get its size), then produces a set of corrected points that represent the image as it was before a photograph was taken of it. It is an integral part of area calculation, as it can determine how large each area should be relative to all of the others given distance from the camera, etc.

For SquirrelGPU, the entry point for this algorithm is stored in class pCorrectJavaFallback. This class contains only one method: transformImage(), which accepts various data and corrects an image file stored on the device. A detailed description of all classes and algorithms follows:

class pCorrectJavaFallback:
public void transformImage()
Args: pCorrectCamera camera, String infile, String outFileLocation, double	totalViewAngle.
Description: Corrects the image given various data contained in the pCorrectCamera and	totalViewAngle.
Algorithm:
Declare variables, including the input plane, intermediate plane, and an array of	output points that will represent the various stages of correction.
Load the input image.
Get the height and width of the image.
Triangulate how far away the camera is from the original image plane.
Set various camera data for the correction. Set the roll to 0 to prevent further	unnecessary distortion, and set azimuth to 270 to simulate the camera	being on the other side of the image plane, so that it may get an inverse	image.
Set the x and y coordinates for the new, inverted camera.
Set the points on the input plane that will represent the vertices of the unchanged	image.
Produce an intermediate plane from the input plane. This produces a 3d plane	from the original 2d image plane.
Calculate the 2d corners for the output image.
Set the new image size to the original times some scaling factor.
Create a double array from the original photo vertices.
Create a double array from the corrected vertices.
Apply a transformation.
Write the final image to storage.
End class pCorrectJavaFallback.

Class pCorrectCamera:
Public data:
double roll, azimuth, pitch, height, x, and y.
public void invertCamera()
Args: none.
Description: Inverts various values to produce a final inverted camera.
Algorithm:
Increase pitch and roll by 180 degrees.
Set the azimuth equal to 90 degrees.
public void adjPitch()
Args: none.
Description: Not used. Was originally going to be used to keep the pitch within a	reasonable range.
Algorithm:
if the pitch is greater than 360 degrees:
then decrease it by 360 degrees.
End class pCorrectCamera.

Class pCorrectPoint:
Public data:
double x, y, z.
Constructor 1:
Args: none
Description: Sets all internal data to 0.
Algorithm:
Set x, y, and z to 0.
Constructor 2:
Args: double newX, newY, newZ.
Description: Sets all internal data to the args. Not used.
Algorithm:
Set x to newX.
Set y to newY.
Set z to newZ.
End class pCorrectPoint.

Class pCorrectPlane:
Public data:
int totalX, totalY.
pCorrectPoint imagePointArray[][].
Constructor:
Args: none.
Description: Was originally used to produce a pCorrectPlane of a certain size. This is	now used to produce a pCorrectPlane made up of four pCorrectPoints.
Algorithm:
Initialize two loop counters.
Initialize imagePointArray as a new pCorrectPoint of size 2, 2.
Loop through and initialize every value in imagePointArray.
public pCorrectPlane returnIntermediatePlane()
Args: pCorrectCamera cam, double camDistFromPlane.
Description: Given the input camera and distance from the plane, follow the first set of	equations listed on the following page:	http://en.wikipedia.org/wiki/3d_projection#Perspective_projection
to build an intermediate 3d plane of image points that will later be	converted to 2d points.
Algorithm:
Declare the output plane, two loop variables, and three Euler angles (as doubles).
Convert the Euler angles (x, y, and z) to the radian values of cam.pitch, cam.roll,	and cam.azimuth. This step will save computational time.
Loop through, and for each iteration:
Print out the point at the loop location.
Perform a lot of messy trigonometry on the x, y, and z of the intermediate	plane's imagePointArray.
End loop.
Return the intermediate plane.
public pCorrectPoint[] calcCorners()
Args: pCorrectPlane input, pCorrectCamera inCam.
Description: Calculates the final 2d points given a 3d plane and various camera data.
Algorithm:
Declare various loop variables, temporary values, and an output array of	pCorrectPoints.
Loop through and for every value:
Initialize the pCorrectPoint.
End loop.
Loop through and print out every input point for debugging purposes.
Perform some messy calculations to get the vertices.
Sanity check the coordinates so that they aren't located off the left edge of the	output image.
Push the height of the image to PerspectiveTransformationEngine.
Return the pCorrectPoint array.
End class pCorrectPlane.